## Slide 1: Innovations in borehole image data acquisition and processing
Timo korth
Advanced Logic technology sa
ASEg 2015

## Slide 2: Motivation
~100 slim hole ATV / OTV tools released to the market every year
Several hundred kilometers of image logs are acquired yearly in the mining industry alone
1995
2015
Image logging has been fully accepted by the industry
60+ years of research and development in (ATV) image logging

## Slide 3: Contents
Introduction
Acoustic Televiewer ( ATV) and Optical Televiewer (OTV) tools today?
What is the latest in data processing software?
Conclusion

## Slide 4: Introduction (cont.)
Where does Image Logging fit in?
Radioactive
Ultrasonic
Optical
Electrical
Limite
Limited
Resolution
Limited
Coverage
Orientation?

## Slide 5: Introduction (cont.)
Latest in Acoustic (ATV) & Optical Televiewer (OTV) Technology
Travel Time
Reflected Amplitude
True Color Image
Motor
Focusing Mirror
Transducer
LED Light
CMOS Sensor
Lens

## Slide 6: ATV - Tools & Benchmarks
 | ATV 9804 (Century) | USS (Raax) | HRAT (RG) | ABI 42 (Electromind) | ABI 40-2G, 43, 85 (ALT sa)
Diameter [mm] Length [m] Weight [kg] | 50.8 2.25 14 | 50 0.93 - | 42 1.62 - | 42 2.1 10 | 40, 43, 85 (92) 1.61, 1.7, 5.2 6.7, 10, 150
Max. Temp [°C] Max. P [bar] | 85 105 | 50 50 | - - | 70 150 | 70, 125 (175), 300 200, 800, 700 (1400)
Circ. Res. [pts] Vert. Res. [mm] | 256 5 | - - | 360 (var.) - | 360 (var.) - | 360 (var.) 1.5
Transducer Freq. [MHz] | - | 1.0 | 1.5 | 1.5 | 1.2
Sensor Rotation Rate per sec. | 12 | - | 20 | 20 | 35
Max. Op. Diam. [mm] | 230 | 148 | 380 | - | 600
Orientation | Magnetic, G | Mech. Compass | Magnetic, G | Magnetic, G | Magnetic, G
Stackable | +GR | No | + GR | + GR | Yes (40, 43)
Logging Speed [m/min] | 3 | 0.6 | 2.5 @ 180 pts, 3mm | 2.5 @ 180 pts, 3mm | 6-7 @ 144 pts, 3mm

## Slide 7: Overcoming the Bottleneck
Natural limit to logging speed imposed by signal travel time through fluid.
Solution: Acquire other data in the same run using stackable logging tools.
12 rev/sec
32 rev/sec
man. gate
auto gate
7 m/min @ 4mm, 144 pts
4 m/min @ 2mm, 144 pts

## Slide 8: Innovation Hidden in Details
Sophisticated digital signal processing (downhole) allows
Signal cleaning (e.g. tool window reflection filter)
Signal separation (e.g. multiple echo detection)

## Slide 9: OTV - Tools & Benchmarks
 | ODS (Raax) | Hi-OPTV (RG) | OBI 52 (Electromind, Geovista) | OBI 40 - 2G (ALT sa)
Diameter [mm] Length [m] Weight [kg] | 50 1.03 - | 52 1.63 - | 52 1.63 5 | 40 1.47 5.3
Max. Temp [°C] Max. P [bar] | 40 - | 60 100 (200) | 60 100 (200) | 70 200
Circ. Res. [pts] Vert. Res. [mm] | 720 0.25 | 1440(var.) Limited by depth encoder | 1440(var.) Limited by depth encoder | 1800 (var.) Limited by depth encoder
Sensor | Camera | 24 bit CMOS | 24 bit CMOS | 24 bit CMOS
Max. Op. Diam. [mm] | 200 | 300 | 300 | 530
Orientation | Mech. Compass | Magnetic, G | Magnetic, G | Magnetic, G
Stackable | No | + GR | +GR | Yes

## Slide 10: Resolution
 | CORE SCAN [pixels/mm] | pixels/mm @ 900 pixels | pixels/mm @ 1440 pixels | pixels/mm @ 1800 pixels
NQ (75.7 mm) | 5 – 40 (360) 5 – 10 (Box) | 4 | 6 | 8
HQ (96 mm) |  | 3 | 5 | 6
PQ (122.6 mm) |  | 2 | ~4 | 4
Logging Speed [m/min] | ~ 3 | 6 @ 2 mm | ~2.5 @ 1 mm | ~1.5 @ 1 mm
International Grain Size Classification (ISO 14688-1)
Name | Size range (mm)
Large boulder | >630
Boulder | 200 – 630
Cobble | 63 – 200
Coarse gravel | 20 – 63
Medium gravel | 6.3 – 20
Fine gravel | 2.0 - 6.3
Coarse sand | 0.63 - 2.0
Medium sand | 0.2 - 0.63
Fine sand | 0.063 - 0.2
Coarse silt | 0.02 - 0.063
Medium silt | 0.0063 - 0.02
Fine silt | 0.002 - 0.0063
Clay | ≤0.002

## Slide 11: Data Processing Software - Trends
Colorimetry
Extract chromatic data like Red, Green, Blue, Luminance, Saturation and Hue
Integration of chromatic changes with stratigraphic, geochemical, wire-line or other geologic data
OTV
Luminance
Hue

## Slide 12: Data Processing Software – Trends (Cont.)
Colorimetry
Separation of Mineral Phases
Grain size distribution
Porosity

## Slide 13: Data Processing Software – Trends (Cont.)
Task optimized workspaces
Guidance & Objectivity
Structure Workload
Manual and Auto Picking
Corrected Dips, Representative Dips
Interpretation,
Classification

## Slide 14: Data Processing Software – Trends (Cont.)
Representative Pick Determination
Clustering based on Depth, Dip, Azimuth and Confidence
Before Clustering
After Clustering of “Blue” and “Grey”

## Slide 15: Conclusion
Changes in user profile towards “App User” !?
User to be driven by innovation?
User to drive innovation?
Invitation to provide feedback and play a role in future innovations.
Motivation

## Slide 16
Questions ?