## Slide 1: Comparing AEM with lithological data using a comprehensive database system for geological and downhole geophysical information
Esben Auken, Professor HydroGeophysics Group, Aarhus University, Denmark

## Slide 2: Co-workers
Cyril Schamper, Paris IV University, France
Flemming Jørgensen, GEUS
Ingelise Mølller Balling, GEUS
Flemming Effersø, SkyTEM Surveys Aps
Kurt Sørensen, SkyTEM Surveys Aps and Aarhus University
Casper Kirkegaard, HydroGeophysics Group, Aarhus University
Anders V. Christiansen, HydroGeophysics Group, Aarhus University
(GEUS – Geological Survey of Denmark and Greenland)

## Slide 3: Outline
GERDA and Jupiter – data management system on corporate and nation level
Borehole logs as a prof of resolution for new AEM system

## Slide 4: Why bother about databases?
Database – datamodel – ensuring data consistency
Web based access or direct client access
SQL for resorting and querying data

## Slide 5: GERDA – Geophysical Data
Raw data
Processed data
Models
Meta data
GERDA
Oracle or Firebird on corporate level
Microsoft Access on client level

## Slide 6: GERDA – Geophysical Data
Raw data
Processed data
Models
Meta data
GERDA
Established 1998
+50 000 groundbased TEM soundings
+40 000 line km SkyTEM
+10 000 km ERT
+200 geophysical logs
+5000 VES soundings
?? Km HEM and GCM
1D layered models
2D models
Geo reference data

## Slide 7: GERDA + Jupiter – Geophysical Data
Raw data
Processed data
Models
Meta data
Lithology
Pressure head
Geochemistry
Meta data
GERDA
Jupiter
Archive established 1926
+280 000 boreholes
Data quality is varying

## Slide 8: GERDA + Jupiter – Geophysical Data
Raw data
Processed data
Models
Meta data
Lithology
Pressure head
Geochemistry
Meta data
GERDA
Jupiter
Data access from www and
modelling programs

## Slide 13: Why bothering about databases?
Database – datamodel – ensuring data consistency
Web based access or direct client access
SQL for resorting and querying data
GERDA is a well structured data georeferenced exchange format
Data is added by contractors and extracted by clients
Møller, I., Søndergaard, V.H. ,Jørgensen, F., Auken, E, & Christiansen, A.V, 2009
Integrated management and utilisation of hydrogeophysical data on a national scale. Near Surface Geophysics, 7, 647-659.

## Slide 14
SkyTEM data

## Slide 15: Aarhus Workbench
AARHUS WORKBENCH
DATABASE
GIS

## Slide 16: Aarhus Workbench
AARHUS WORKBENCH
DATABASE
GIS
DATA IMPORT
TEM
GCM
ATEM
HEM
ERT/IP
Models
XYZ files

## Slide 17: Aarhus Workbench
AARHUS WORKBENCH
DATABASE
GIS
DATA IMPORT
TEM
GCM
ATEM
HEM
ERT/IP
Models
XYZ files
DATA PROCESSING
GCM
ATEM
ERT/IP

## Slide 18: Aarhus Workbench
AARHUS WORKBENCH
DATABASE
GIS
DATA IMPORT
TEM
GCM
ATEM
HEM
ERT/IP
Models
XYZ files
DATA PROCESSING
GCM
ATEM
ERT/IP
DATA
INVERSION
GCM
ATEM
HEM
ERT/IP

## Slide 19: Aarhus Workbench
AARHUS WORKBENCH
DATABASE
GIS
DATA IMPORT
TEM
GCM
ATEM
HEM
ERT/IP
Models
XYZ files
DATA PROCESSING
GCM
ATEM
ERT/IP
DATA
INVERSION
GCM
ATEM
HEM
ERT/IP
THEMES & PROFILES

## Slide 20: Aarhus Workbench

## Slide 21: Outline
GERDA and Jupiter – efficient data management system on corporate and nation level
Borehole logs as a prof of resolution for new AEM system

## Slide 22: Nitrate reduction in geologically heterogeneous catchments
Information about the upper 20m critical
Refsgaard, et al.,2014, Nitrate reduction in geologically heterogeneous catchments - A framework for assessing the scale of predictive capability of hydrological models ScienceDirect, 468-469, 1278-1288.

## Slide 23: Area and flight lines
100 m line spacing 13 hours - 1203 km
50 m line spacing 5 hours - 465 km
25 m line spacing 2 hours - 178 km
…1846 km in 1 week
(Aarhus->Barcelona)

## Slide 24: SkyTEM 101
Transmitter loop
Receive coil
Instruments
Generator
GPS,
Tilt
Lasers
Turn-off time low moment ~4 µs
First gate ~5-6 µs; ~1-2 µs after turn-off
LM measured every 0.6 s (~ 80 stacks)
Lateral resolution 15 m
Loop area ~130 m²
Speed +100 km/h
Nominal flight altitude: 30 m

## Slide 25: Dual moment deep and near surface investigation
Time [s]
1e-06
1e-05
1e-04
1e-03
1e-02
1e-01
dB/dt [V/m^2]
1e-09
1e-08
1e-07
1e-06
1e-05
Deep information
Near surface information
Noise
2 decays in time - 5 decays in signal
High Moment (HM)
Low Moment (LM)

## Slide 26: Profile South-North
Glacial valley
Palaeogene clay
Sand layers
(Smooth SCI with 29 layers + 3D gridding)
Clay
Sand
S
N
Mean resisitvity map 15-20 m
Clay lenses
Glaciotectonic
complex
Resistivity (Ωm)
0.1
10
1
100
1000

## Slide 28: Profile West-East: the very near surface
Sand layer of 5-10 m
Clayey lens
Small buried valley
(Smooth SCI with 29 layers + 3D gridding)
W
E
Glaciotectonic complex
Clay
Sand
Resistivity (Ωm)
0.1
10
1
100
1000

## Slide 29: SkyTEM 101 versus lithological logs
I = clay
ml = moraine clay
s = sand
ds = glacial sand
g = gravel
W
E
(Smooth SCI with 29 layers + 3D gridding)
Clay
Sand
Resistivity (Ωm)
0.1
10
1
100
1000

## Slide 30: SkyTEM 101 versus lithological logs
(Smooth SCI with 29 layers + 3D gridding)
I = clay
ml = moraine clay
s = sand
ds = glacial sand
g = gravel
Clay
Sand
Resistivity (Ωm)
0.1
10
1
100
1000

## Slide 32: SkyTEM 101 versus lithological logs
Final statistics (46 boreholes < 15 m from SkyTEM soundings)
44 % with very good match
33 % with good match
17 % with poor match
6 % which disagrees
Reasons of mismatches (poor and disagrees – 23%)
  Borehole data, quality of samples and descriptions/geological interpretations (37 %)
  Vertical geological variations, vertical resolution (23 %)
  Lateral geological variations, horizontal resolution (17 %)
  Borehole coordinates (13 %)
  Other/unknown (10 %)
Schamper, C., Jørgensen, F., Auken, E., and Effersø, F.,2014, Assessment of near-surface mapping capabilities by airborne transient electromagnetic data - An extensive comparison to conventional borehole data Geophysics, 79, B187-B199

## Slide 33: Conclusion
Databases ensures data consistency
Data are georeferenced and meta data are stored in well described format
Data exchange on the internet from contractors to clients
SkyTEM 101 versus lithological logs show excellent correlation

## Slide 34
Thank you for your attention