## Slide 1: Monte Carlo (stochastic) inversions - similarities and differences to gradient based methods
Ross C Brodie, Geoscience Australia

## Slide 2: Probabilistic framework - similarities and differences to the deterministic framework Direct search methods - similarities and differences to gradient based methods
Or should that have been?

## Slide 3: Outline
Frameworks: Deterministic and probabilistic
Methods: Gradient based and direct search
Compare and contrast
Example

## Slide 4: Declaration
Many of the illustrations in this presentation are supplied with permission from, and courtesy of, Malcolm Sambridge, Research School of Earth Sciences, Australian National University.

## Slide 5: Inversion frameworks
Deterministic framework
  often called an optimization approach or problem
  concerned with finding a single solution
  usually the global extremum (max or min) of an objective function
Probabilistic framework
  often called probabilistic inference, ensemble inference, or Bayesian inference approaches
  concerned with estimating the statistical distribution of feasible solutions
  usually finds solutions in the vicinity of the global extremum plus several local extremum of an objective function

## Slide 6: Crux of the difference between the frameworks
Image of Log Likelihood or Negative of data misfit
Samples from the Posterior Probability Density Function
Deterministic framework
Probabilistic inference
The answer

## Slide 7: Posterior Probability Density Function (PDF)
Deterministic framework is concerned with locating, for example, the peak of the posterior PDF histogram
Probabilistic framework seeks to estimate the whole shape of the posterior PDF histogram

## Slide 8: Methods of finding the solution(s)
Gradient based methods
Direct search methods
  Non Monte Carlo
  Monte Carlo

## Slide 9: Gradient based methods
Basic idea is to traverse down the objective function surface using the slope direction (vector gradient) as guidance on the direction in which to go
Data forward model must be differentiable (analytically or numerically) w.r.t. the unknown model parameters
Works for many unknowns (dimensions)
Only used in the deterministic framework
Ideal for linear model-data relationships
Work for weakly non-linear problems by iterative solution and linearizing about the current model… but can fail
Fails for strongly non-linear problems
e.g. steepest descent, conjugate gradients, (quasi) Newton methods

## Slide 10: Monte Carlo methods
Involves the use of random numbers and trials
  Not typically suitable for large number of unknowns
  Favoured method of sampling an unknown Posterior PDF
Used in the deterministic framework
  Uniform random search, Simulated annealing, Evolutionary and Genetic algorithms (GA)
Also used in the probabilistic inference framework
  Neighbour algorithm (NA)
  Markov Chain Monte Carlo (McMC)
  Reversible-jump Markov Chain Monte Carlo (rj- McMC)

## Slide 11: Crux of the difference between methods
Image of Log Likelihood or Negative of data misfit
Samples from the Posterior Probability Density Function
Iteration 6
Final solution
Iteration 0
Initial guess
Iteration 3
Gradient based method
Monte Carlo sampling

## Slide 12: Linear data-model relationship
Quadratic objective function surface
Single minimum
Gradient based methods are the most suitable solution method
Monte Carlo methods are not justified

## Slide 13: Weakly non-linear data-model relationship
More complicated objective function surface
Multiple minima
Gradient methods are possible by linearizing the problem
Gradient methods can get stuck in local minima, whereas Monte Carlo methods can climb out of local minima and explore multiple feasible regions

## Slide 14: Strongly non-linear data-model relationship
Extremely complicated objective function surface
Multiple minima
Gradient based methods are useless
Monte Carlo methods can give good results

## Slide 15: Derivatives
Gradient based methods require that the data forward model must be differentiable (analytically or numerically) with respect to the unknown model parameters.
Monte Carlo methods do not in general require derivatives
Monte Carlo methods can thus usually be applied to more complex data-model relationships and it is easier to use more sophisticated objective functions
Monte Carlo do not require large memory matrix inversions or solvers
Monte Carlo methods are often easier to code up

## Slide 16: Number of unknowns
Gradient based methods can handle millions of unknown parameters to be solved for
The amount of work to be done in Monte Carlo methods increases with the power of the number unknowns
Monte Carlo methods are thus usually only suited to problems with less than 10s or perhaps 100s of unknowns
What about software like GeoModeller? ... it is more a model refinement code than a full parameter search algorithm

## Slide 17: Computation time
Monte Carlo methods require vastly more computation time than gradient based methods for optimization problems
This is even more pronounced for the probabilistic inference framework where we wish to properly sample the posterior PDF
For example, the deterministic gradient based inversion of a single 1D time domain AEM sounding may take ~3 seconds but may take about 30 minutes or more to perform, a full probabilistic inference rj-McMC inversion

## Slide 18: Uncertainty
There are good methods for estimating uncertainty, trade-offs and resolution for gradient based linear problems - e.g., from the posterior model covariance and resolution matrices
These can also be applied to weakly non-linear problems but the uncertainty estimates will not necessarily be accurate
Uncertainty estimates are biased by the regularization that is applied and are likely to be overly optimistic
Probabilistic inference methods provide a more robust means of estimating uncertainty and non-uniqueness than deterministic methods

## Slide 19: Non-uniqueness
A small subset of 3 (left) and 15 layer models (right) that all fit the synthetic data within the prescribed noise levels

## Slide 20: rj-McMC AEM inversion outline
Reversible-jump Markov chain Monte Carlo (rj-McMC)
Generate an ensemble of 100,000s of models that fit the data - i.e., not just a single model as in deterministic inversion
Reversible-jump (or transdimensional) means that the algorithm automatically changes the number of layers
The ensemble is generated via Markov chain importance sampling
New models are proposed by randomly perturbing the last link (model) in the chain

## Slide 21: rj-McMC inversion - proposal types
Four types of model update may be proposed at each link in the chain
Insert Title Here <view/master/slidemaster>
interface move
1/6
layer birth
1/6
layer death
1/6
Ross C Brodie DGAL 2012: From little things big things grow
conductivity change
1/2

## Slide 22: rj-McMC inversion - importance sampling
We don't just accept any old proposed model, they are rejected from or accepted onto the end of the Markov chain based on an acceptance probability
All other things being equal, this means proposed models are more likely to be accepted if they
  fit the data better than the current model
  are more different from the current model
  are more similar to the a priori information
  have fewer dimensions (layers)
We end up with an ensemble of simple models that fit the data as well as being consistent with the prior information
Ross C Brodie DGAL 2012: From little things big things grow

## Slide 23: rj-McMC inversion - importance sampling
And theoretically (cross your fingers and with any luck) the ensemble will eventually converge to a statistical distribution that matches the true posterior PDF of the model given the prior information and the new data
Ross C Brodie DGAL 2012: From little things big things grow

## Slide 24
low moment data and error bars
high moment data and error bars
low moment forward model - not yet fitting
high moment forward model - not fitting yet
acceptable data misfit below here
end of the burn-in period
histogram of number of layers
last model in the Markov chain

## Slide 26
Ross C Brodie DGAL 2012: From little things big things grow

## Slide 27
Ross C Brodie DGAL 2012: From little things big things grow

## Slide 28: Deterministic gradient based - smoothness
low smoothness
medium smoothness
high smoothness

## Slide 29: Deterministic gradient based - reference model
reference conductivity 0.001 S/m
reference conductivity 0.050 S/m

## Slide 30: Deterministic grad based and rj-McMC comparison
deterministic -medium smoothness
rj-McMC -
most probable (best) model
rj-McMC -
mean model

## Slide 31: Location A

## Slide 32: Location B

## Slide 33: Location C

## Slide 34: Conveying uncertainty on depth slice images

## Slide 35: Acknowledgements
Malcolm Sambridge, Research School of Earth Sciences, Australian National University, for guidance on the Monte Carlo inversion algorithm.
National Computational Infrastructure (http://www.nci.org.au) which we used for the computational work.
Western Australia Department of Water for providing the Lake Thetis example dataset.

## Slide 36: Monte Carlo (stochastic) inversions - similarities and differences to gradient based methods
Ross Brodie, Geoscience Australia