| Ferret Borehole Magnetometer Magnetics in the 3rd Dimension Detect and delineate magnetic igneous intrusions both in and off hole. Investigate beneath magnetic overburden. Innovative, fast sampling Overhauser Effect Magnetometer designed for borehole applications to a depth of 600 metres. Designed to compliment ground and airborne magnetic surveys. 300 times more sensitive than conventional downhole, fluxgate magnetometers which allows for the unprecedented detection of off hole intrusions. Deployed on a standard wireline logging system allowing rapid magnetic data acquisition and processing in conjunction with routine geophysical borehole logging. Data are corrected to an online reference base station magnetometer. Sensor, electronics and power supply are self-contained within the tool. Does not require any radioactive sources. Operates both in air and fluid filled boreholes. Diurnal reduction software with LAS output. |  |
| --- | --- |

New Product

| Ferret Borehole Magnetometer Specifications Magnetic Measurement Total field Resolution 0.05nT @ 2Hz Diameter 78mm Length 1.3m Maximum operating depth 600m Wireline standoff for 0.05nT heading error 8m Memory 2 meg Cycle speed <= 2 Hz Battery 12V rechargeable GEL cell. Operating time @ 2Hz 12 Hours Weight 6Kg Housing Nonferrous, nonconductive custom wound glass fibre & dalrin. |  |  |
| --- | --- | --- |
| Manufactured by Ultramag Geophysics | 6 Eagles Nest Close BELMONT NORTH NSW 2280 AUSTRALIA Tel (02) 4942 8400 Fax (02) 4942 8402 Http://www.ultramag.com phil@ultramag.com |
| Survey services by |  |